## Slide 1: Compact OCT scanner for a bimodal endoscopic probe
Sergio Vilches

## Slide 2: Motivation Bimodal Endoscopy
Arteriovenous Malformation
Fujii T. Kuwano H.
Transversal OCT image of the macula J. A. Flatter and J. Carroll,
OCT
microscopy
+
Notes: Add 3.5 mm jack
Motivation: use several imaging modalities to improve diagnostic
Proposed endoscope head 13x2x3mm3
Aim of thesis: OCT modality
-> Review theory of OCT

## Slide 3: Swept-Source Optical Coherence Tomography SS-OCT Theory
Michelson interferometer
Spectrogram
Fourier transform
sample
reference
mirror
Notes: What is SS-OCT?
Technique to measure depth information of a sample by analyzing its backscattered light.
Michelson interferometer with a laser which can sweep its wavenumber.
Intuitive explanation: Imagine reflector in sample arm
  If placed at same distance as reference arm: constructive interference at all wavelengths
  If placed at z1, some wavelengths constructive, other destructive
  Spectrogram modulated by distance

## Slide 4: Swept-Source OCT: Fiber Scanner Implementation
Optical requirements:
Long depth of field
Mechanical requirements:
Scanning mechanism
Slow scanning speed
Telecentric
Notes: OCT systems endoscopy: fiber based
Same components but now probe goes into body
Practical requirements: Low NA 0.02

## Slide 5: Fiber scanner Bimodal implementation
Notes: Proposed implementation of bimodal probe
2 layer design
  Independent beampaths, combined by dichroic beamsplitter
  Ensure registration of both fields
System size of headphone jack
-> Analyze scanning engine, unfold the path

## Slide 6: Fiber scanner Fourier plane scanner
Fourier plane
Notes: Chosen implementation: Fourier plane scanner
Developed by Eric Seibel 2000
Intermediate region of a conventional microscope
Emulate this behavior by collimated light at an angle
-> How to achieve this behavior?
[Remove dashed angled line]

## Slide 7: Fiber scanner Piezoelectric actuation + Mechanical amplification
Notes: Piezoelectric actuation + Mechanical amplification
Piezoelectric tube: 4 electrodes, fixed at base
Excites a cantilever formed by fiber+GRIN
Sinusoidal excitation at fres -> 1000x mechanical gain
-> Lower fres as much as possible: analytical calculation

## Slide 8: Fiber scanner Resonance frequency estimation
COMSOL Simulation:
762 Hz
Analytical Calculation
770 Hz
Notes: Estimation by modelling the GRIN as point weight
Dependance: Dfiber, length, mas
-> Optical analysis of the scanner

## Slide 9: Optical performance Geometrical optics
Parameter | Value
NAfiber | 0.18
fGRIN | 0.2
dbeam | 0.3
fobj | 7.5
NAOCT | 0.022
Notes: Geometrical optics:
Interrelated parameters
Set NA
Calculate resolution of such system
  OCT: Illuminate with laser, collect light

## Slide 10: Optical performance Fourier optics: illumination PSF
Infinitesimal fiber core
Gaussian mode fiber core
Notes: Start considering illumination: projector
  Fiber - lens - aperture – sample
  If fiber is point source – PSF shape defined by optics (NA), beam diameter
  If fiber has an extended mode shape: convolution of
-> What happens with backscattered light?

## Slide 11: Optical performance Fourier optics: illumination + collection
illumination
detection
23.3 lp/mm
43 µm
Notes: Helmholz reciprocity: Folded optical system
In order that photon reaches the detector:
  Illuminate inside PSFill
  Be accepted into the optical system
  Same PSF squaring
Squaring of PSF – Autocorrelation of MTF
-> Simulation of this behavior

## Slide 12: Optical performance ZEMAX simulation: Geometrical raytracing
spot through focus
raytracing
1.2 mm
Notes: Different fields
Spot through focus
Aberrations
Low NA
1.2 mm FOV
-> Analyzed, simulated -> Test its behavior

## Slide 13: Implementation Single modality probe
Notes: Implementation of single modality, OCT probe
Equivalent optics, mechanics
3D printed housing
Custom PI interconnects

## Slide 14: Experimental evaluation Laser scanned imaging
1.2 mm
Notes: Experimental evaluation: Obtain Laser Scanned Images
Measure intensity of backreflected light
Setup
2D area: spiral scanning
FOV

## Slide 15: Experimental evaluation Distortion correction
Whirl patterns
Distortion Correction
Notes: Distortion:
Non ideal beam: 2 axes of symmetry: eigendirection
Cross coupling of energy between them
Whirling
Solution:
  WP far from resonance but enough gain
  Look up table measured with PSD

## Slide 16: Experimental evaluation Resolution and field of view
Lateral resolution: 48 µm
Depth of Field: 3.5 mm
Edge Spread Function
MTF
Translated mirror
,
Notes: Evaluate resolution:
Lateral resolution:
  Edge (derivative) PSF (fourier) MTF

## Slide 17: Experimental evaluation OCT cylindrical cross section imaging
Human fingertip
Human colon polyp

## Slide 18: Conclusion and Outlook OCT 2D Imaging
OCT scanning engine: 0.9 mm diameter, 9 mm length
  → Smallest in literature?
Accurate optical and mechanical analytical analysis
  → Guideline for future fiber scanner systems
Reduction of imaging distortions
Outlook: Integration in bimodal probe

## Slide 19: Compact OCT scanner for a bimodal endoscopic probe
Sergio Vilches

## Slide 20: Implementation Electrical contacts

## Slide 21: Implementation 3D printed housing